## Slide 1
MOLECULAR BIOLOGY · CORE LABORATORY TECHNIQUES
PCR, Electrophoresis,
Centrifugation & Radiotracers
A comprehensive, comparison-driven walkthrough of the four technique families that underpin every molecular biology laboratory — their physical principles, workflows, variants and the exact points on which they differ.
Notes: Overview deck covering PCR and its variants, electrophoretic separations, centrifugation and radioisotope tracer techniques. Emphasis throughout is on what distinguishes each method from its neighbours.

## Slide 2
ROADMAP
Four Families of Technique — One Logic
Every technique below does one of two jobs: it AMPLIFIES a signal so a rare molecule becomes detectable, or it SEPARATES a mixture so one component can be measured. Keep asking of each method: what property is it sorting on?
PCR & Variants
Amplify. Conventional · Nested · RT-PCR · Real-time (qPCR) · Digital PCR. Sorting property: sequence identity of the primer sites.
MODULE 01
Electrophoresis
Separate in a gel. Agarose · SDS-PAGE · IEF · 2D-PAGE. Sorting property: charge, size and shape in an electric field.
MODULE 02
Centrifugation
Separate in a field of force. Differential · Rate-zonal · Isopycnic. Sorting property: sedimentation coefficient and buoyant density.
MODULE 03
Radiotracers
Detect and follow. Labelling · scintillation · autoradiography. Sorting property: none — it is a detection layer over the others.
MODULE 04
How they chain together in a real experiment
Tissue or culture → homogenise and fractionate by CENTRIFUGATION (get the right organelle or clean nucleic acid) → extract DNA / RNA / protein → amplify the nucleic acid by PCR / RT-qPCR, or resolve the protein by SDS-PAGE / 2D-PAGE → read out the result by ELECTROPHORESIS, fluorescence, or an ISOTOPIC label → quantify.
No single technique answers a biological question on its own; the skill being taught here is choosing the right combination and knowing what each step can and cannot resolve.
Notes: Frame the deck around the amplify-versus-separate distinction, and the sorting property of each family. Students who hold on to "what property is being sorted?" rarely confuse these methods later.

## Slide 3
01
Polymerase
Chain Reaction
Kary Mullis, 1983 · Nobel Prize in Chemistry, 1993. An in vitro, primer-directed, enzymatic amplification of a defined DNA segment.
1
Components, the three-step thermal cycle and amplification kinetics
2
Nested PCR — two rounds, two primer pairs, geometric gain in specificity
3
Reverse transcription PCR — from RNA to cDNA, one-step vs two-step
4
Real-time (quantitative) PCR — Ct, chemistries and quantification maths
5
Digital PCR and a master comparison of all variants

## Slide 4
MODULE 01 · PCR
The Core Idea and the Reaction Mixture
PCR replicates a chosen DNA segment in vitro. Two primers define the boundaries of the product; a thermostable polymerase copies between them; a thermal cycler supplies the temperature changes that a helicase would supply in vivo. Each cycle doubles the target, so n cycles give a theoretical 2ⁿ-fold gain.
Template DNA
10 pg – 1 µg of genomic DNA (≈ 10–100 ng typical). Purity matters more than amount — haem, humic acid, EDTA and phenol are classic inhibitors.
Primer pair
Forward + reverse, 18–25 nt, 0.1–0.5 µM each. They alone decide WHAT is amplified and how long the amplicon is. Specificity of the whole reaction lives here.
Thermostable polymerase
Taq (Thermus aquaticus): t½ ≈ 40 min at 95 °C, 5′→3′ exo⁺, NO 3′→5′ proofreading, error ≈ 1 × 10⁻⁴/base. Pfu / Phusion / Q5 proofread — use for cloning and sequencing.
dNTPs
200 µM each of dATP, dTTP, dGTP, dCTP. Must be equimolar — an unbalanced pool raises the misincorporation rate. dNTPs also chelate Mg²⁺.
Mg²⁺ (MgCl₂)
1.5–2.5 mM. Essential cofactor — forms the dNTP–Mg complex the enzyme actually uses. Too little → no product; too much → non-specific bands. The first thing to titrate.
Buffer & additives
10 mM Tris-HCl pH 8.3, 50 mM KCl. GC-rich or structured templates: 5–10 % DMSO, 1 M betaine, or 7-deaza-dGTP to lower the melting temperature.
Taq polymerase has no proofreading exonuclease — that single fact explains why cloning-grade PCR uses a different enzyme, and why long amplicons accumulate errors.
Notes: Ask students which single component they would titrate first when a reaction gives smeary non-specific product: the answer is Mg2+, then annealing temperature.

## Slide 5
MODULE 01 · PCR
The Three-Step Thermal Cycle
One cycle = denature → anneal → extend, repeated 25–40 times. Flanking the cycles are an initial denaturation and a final extension, neither of which is part of the repeating loop.
STEP 1
Denaturation
94–95 °C, 20–30 s
Hydrogen bonds between the strands break; duplex → two single strands. GC-rich targets need the higher end. Too long or too hot destroys Taq.
STEP 2
Annealing
50–65 °C, 20–40 s
Primers base-pair with their complementary sites. Set Ta ≈ Tm − 5 °C. Too low → mispriming and extra bands; too high → no product.
STEP 3
Extension
72 °C, ~1 min per kb
Taq optimum. Polymerase adds dNTPs 5′→3′ from each primer’s free 3′-OH, at ≈ 1–2 kb/min, copying the template strand.
↻ Repeat 25–40 times
Chart: Temperature (°C)
| start
Block temperature (°C) | 95 | 95 | 55 | 55 | 72 | 72 | 95 | 95 | 55 | 55 | 72 | 72 | 95 | 95 | 55 | 55 | 72 | 72
Temperature profile across three cycles — 95 °C → 55 °C → 72 °C, repeated.
The steps that sit outside the loop
Initial denaturation — 95 °C, 2–5 min: fully melts genomic DNA and activates hot-start (antibody- or chemically blocked) enzymes.
Final extension — 72 °C, 5–10 min: completes partial products and lets Taq add the 3′-A overhang used in TA cloning.
Hold — 4–10 °C indefinitely.
Hot-start prevents primer-dimer and mispriming during room-temperature set-up, when primers can anneal non-specifically.
Notes: Stress that only from the third cycle onward does the discrete, primer-to-primer amplicon appear; cycles 1 and 2 make variable-length products running off the template end.

## Slide 6
MODULE 01 · PCR
Amplification Kinetics and Primer Design
Yield is not infinite: N = N₀(1 + E)ⁿ, where E is the per-cycle efficiency (E = 1 gives perfect doubling). Real reactions leave the exponential phase long before the last cycle — which is exactly why end-point PCR cannot be quantitative.
Chart: Cycle number
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35
log₁₀ product | 0 | 0.30103 | 0.60206 | 0.90309 | 1.2041 | 1.5051 | 1.8062 | 2.1072 | 2.4082 | 2.7093 | 3.0103 | 3.3113 | 3.6124 | 3.9134 | 4.2144 | 4.5154 | 4.8165 | 5.1175 | 5.4185 | 5.7196 | 6.0206 | 6.3216 | 6.6227 | 6.9237 | 7.2247 | 7.5257 | 7.8268 | 8.1278 | 8.4288 | 8.7299 | 9.0077 | 9.1232 | 9.1986 | 9.244 | 9.2699 | 9.2843
Three phases of every reaction
EXPONENTIAL — reagents in excess, efficiency constant and near 100 %. This is the only phase in which product is proportional to starting template, and the only phase qPCR measures.
LINEAR — efficiency falls as dNTPs and primers deplete and Taq loses activity.
PLATEAU — product accumulation stops. Causes: reagent exhaustion, enzyme denaturation, pyrophosphate inhibition, and re-annealing of product strands competing with primers. All tubes plateau at a similar level regardless of input — hence end-point yield tells you almost nothing about starting copy number.
Cycle | 0 | 5 | 10 | 20 | 25 | 30 | 35
Copies of target | 1 | 32 | 1.0 × 10³ | 1.0 × 10⁶ | 3.4 × 10⁷ | 1.1 × 10⁹ | plateau
Length & GC
18–25 nt; 40–60 % GC. Shorter → poor specificity, longer → slow, inefficient annealing.
Tm matched
55–65 °C, and the two primers within 5 °C of each other, or one primer dominates the reaction.
No 3′ complementarity
Self- or cross-complementary 3′ ends give primer-dimers, which out-compete the real target.
GC clamp, no runs
One or two G/C in the last five bases; avoid runs of >4 identical bases and repeats that slip.
Notes: The plateau argument is the single strongest justification for real-time PCR; make sure it lands before moving to qPCR.

## Slide 7
MODULE 01 · VARIANT
Nested PCR — Two Rounds, Two Primer Pairs
Two sequential amplifications. Round 1 uses OUTER (external) primers; a small aliquot of that product becomes the template for round 2, which uses INNER (internal) primers that bind entirely within the first amplicon. The second amplicon is therefore shorter and nested inside the first.
ROUND 1
Outer primers
15–30 cycles with the external pair. Product = long amplicon, together with whatever non-specific products mispriming produced.
TRANSFER
Dilute 100–1000×
Take 1–5 µL into fresh master mix. Dilution removes carried-over primers and dNTPs — and is the contamination-prone step.
ROUND 2
Inner primers
20–35 cycles with the internal pair. Only true target carries BOTH internal sites, so only true target is amplified further.
READ-OUT
Agarose gel
A single sharp band of the expected shorter size. Non-specific round-1 products are diluted out and not re-amplified.
Why specificity rises so steeply
A non-specific round-1 product would have to contain both internal primer sites by chance — vanishingly improbable.
The two rounds multiply, not add: specificity is effectively the product of the two selection events.
Sensitivity reaches single-copy detection, so it suits degraded, ancient, or low-titre samples.
HEMI-NESTED (semi-nested) PCR uses one new internal primer plus one of the original primers — a compromise when sequence data are limited.
Advantages ✓ / Limitations ✕
✓ Very high sensitivity — detects targets below the limit of single-round PCR.
✓ Very high specificity; clean background even from complex templates.
✓ Rescues GC-rich, long or partially degraded templates.
✕ Serious carry-over contamination risk — tubes are opened between rounds (use separate rooms, filter tips, UDG).
✕ Needs more sequence information (two primer pairs).
✕ Twice the time, cost and labour; not quantitative.
Where it is used
Mycobacterium tuberculosis in paucibacillary specimens (CSF, pleural fluid).
Leishmania, Plasmodium, Trypanosoma in low-parasitaemia blood.
HIV proviral DNA and infant diagnosis.
Plant and animal virus detection from field samples.
Forensic and ancient DNA, where template is degraded and scarce.
Metagenomics — recovering rare 16S rRNA phylotypes.
Notes: Contamination control deserves emphasis: nested PCR causes more false positives in diagnostic labs than any other format.

## Slide 8
MODULE 01 · VARIANT
Reverse Transcription PCR (RT-PCR) — RNA → cDNA → PCR
DNA polymerase cannot use RNA as a template. RT-PCR inserts one prior step: reverse transcriptase (an RNA-dependent DNA polymerase) copies RNA into complementary DNA, which then enters an ordinary PCR. It is the standard route to gene expression data and to RNA-virus genomes.
STEP 1
Total RNA / mRNA
Extract with TRIzol or column; DNase I treat to remove genomic DNA; check integrity (RIN ≥ 7) and A260/280.
STEP 2
Prime + reverse transcribe
42–55 °C, 30–60 min. RT extends the primer along the RNA to make an RNA:cDNA hybrid.
STEP 3
Remove RNA / inactivate RT
RNase H nicks the RNA strand; heat 70–85 °C inactivates the RT so it cannot interfere with Taq.
STEP 4
PCR on the cDNA
Normal thermal cycling with gene-specific primers; detect by gel (end-point) or fluorescence (real-time).
The enzymes
AMV RT (avian myeloblastosis virus) — works at 42–58 °C, so it reads through strong RNA secondary structure; higher intrinsic RNase H activity.
M-MLV RT (Moloney murine leukaemia virus) — 37–42 °C, lower RNase H, gives longer cDNA. Engineered RNase H⁻, thermostable versions (SuperScript, Maxima) are the modern default.
Controls that make the result interpretable
NO-RT control — same reaction without reverse transcriptase. Any signal here is amplified genomic DNA, not transcript.
No-template control; primers spanning an exon–exon junction; reference-gene amplification to confirm cDNA quality.
Three priming strategies — the choice determines which RNA becomes cDNA
Oligo(dT)₁₈ — anneals to the poly(A) tail. Only polyadenylated mRNA is copied; clean and specific, but 3′-biased on long or degraded transcripts. Useless for prokaryotic or non-polyadenylated RNA.
Random hexamers — anneal everywhere. Copies all RNA species including rRNA, tRNA, prokaryotic and degraded RNA; gives high cDNA yield but short, fragmented products and dilutes the mRNA signal.
Gene-specific primer — the reverse PCR primer itself. Most specific and most sensitive for one target; but a separate RT reaction is needed for each gene, and no cDNA archive is created.
Notes: The no-RT control is the single most examined point on this topic. Also emphasise that oligo-dT fails on bacterial RNA.

## Slide 9
MODULE 01 · VARIANT
One-Step versus Two-Step RT-PCR
The same chemistry, packaged two ways. In ONE-STEP, reverse transcription and PCR occur in a single sealed tube with a single buffer. In TWO-STEP, cDNA is made first and an aliquot is then used for one or many separate PCRs. Rule of thumb: one target, many samples → one-step; many targets, few samples → two-step.
Feature | One-step RT-PCR | Two-step RT-PCR
Reaction format | RT and PCR in one tube, one buffer, one programme | RT reaction first; cDNA aliquoted into separate PCR tubes
Priming of the RT step | Must use the gene-specific reverse primer (oligo-dT and random primers would prime everything) | Free choice — oligo(dT), random hexamers, gene-specific, or a blend
Enzymes | Blended RT + Taq, or a single thermostable enzyme (e.g. Tth) in a compromise buffer | Each enzyme in its own optimal buffer — both steps can be optimised independently
Contamination risk | Low — the tube is never reopened; ideal for diagnostics | Higher — tube opening and pipetting between steps
Sensitivity | Generally higher for a single target; the whole RT product enters the PCR | Slightly lower per target (only an aliquot of cDNA is used), but adequate
Flexibility | Low — one target per tube; cDNA cannot be stored or reused | High — one cDNA prep serves many genes, repeats and reference genes; cDNA archives at −20 °C
Optimisation & throughput | Fewer pipetting steps, easy to automate; but harder to troubleshoot when it fails | More hands-on time; easier to isolate whether RT or PCR is the failing step
Typical application | Clinical viral load and pathogen detection (SARS-CoV-2, HCV, influenza); high-throughput screening | Gene-expression profiling of many genes, qPCR arrays, cloning full-length cDNA
Notes: Point out that one-step forces gene-specific priming, which students frequently get wrong in exams.

## Slide 10
MODULE 01 · VARIANT
Real-Time PCR — Watching Amplification As It Happens
A fluorescent reporter is included in the reaction and the instrument reads fluorescence at every cycle. Because the reaction is followed while it is still exponential, real-time PCR is quantitative — and because the tube is never opened, carry-over contamination and gel handling disappear.
Chart: Cycle number
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40
10⁶ copies | 0.0024 | 0.0041 | 0.007 | 0.0121 | 0.0208 | 0.0356 | 0.0601 | 0.0998 | 0.1611 | 0.2497 | 0.3659 | 0.5 | 0.6341 | 0.7503 | 0.8389 | 0.9002 | 0.9399 | 0.9644 | 0.9792 | 0.9879 | 0.993 | 0.9959 | 0.9976 | 0.9986 | 0.9992 | 0.9995 | 0.9997 | 0.9998 | 0.9999 | 0.9999 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
10⁴ copies | 0.0001 | 0.0001 | 0.0002 | 0.0003 | 0.0005 | 0.0008 | 0.0014 | 0.0024 | 0.0041 | 0.007 | 0.0121 | 0.0208 | 0.0356 | 0.0601 | 0.0998 | 0.1611 | 0.2497 | 0.3659 | 0.5 | 0.6341 | 0.7503 | 0.8389 | 0.9002 | 0.9399 | 0.9644 | 0.9792 | 0.9879 | 0.993 | 0.9959 | 0.9976 | 0.9986 | 0.9992 | 0.9995 | 0.9997 | 0.9998 | 0.9999 | 0.9999 | 1 | 1 | 1
10² copies | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0001 | 0.0001 | 0.0002 | 0.0003 | 0.0005 | 0.0008 | 0.0014 | 0.0024 | 0.0041 | 0.007 | 0.0121 | 0.0208 | 0.0356 | 0.0601 | 0.0998 | 0.1611 | 0.2497 | 0.3659 | 0.5 | 0.6341 | 0.7503 | 0.8389 | 0.9002 | 0.9399 | 0.9644 | 0.9792 | 0.9879 | 0.993 | 0.9959 | 0.9976 | 0.9986 | 0.9992 | 0.9995
10¹ copies | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0001 | 0.0001 | 0.0002 | 0.0003 | 0.0005 | 0.0008 | 0.0014 | 0.0024 | 0.0041 | 0.007 | 0.0121 | 0.0208 | 0.0356 | 0.0601 | 0.0998 | 0.1611 | 0.2497 | 0.3659 | 0.5 | 0.6341 | 0.7503 | 0.8389 | 0.9002 | 0.9399 | 0.9644 | 0.9792 | 0.9879 | 0.993 | 0.9959
threshold
Anatomy of the amplification plot
BASELINE (≈ cycles 3–15) — signal below instrument detection; used to set background.
THRESHOLD — a fluorescence level placed in the exponential phase, above baseline noise.
Cq or Ct — the (fractional) cycle at which the curve crosses the threshold. This is the measurement.
PLATEAU — ignored entirely; it carries no quantitative information.
What Ct means
Ct is inversely proportional to log(initial template): more starting copies → threshold crossed sooner → lower Ct.
A difference of 1 Ct ≈ a 2-fold difference in template; 3.32 Ct ≈ 10-fold.
Typical dynamic range 7–8 log₁₀ units; sensitivity down to a few copies.
Ct > 35–38 is normally treated as unreliable / below the limit of quantification.
Notes: Make students calculate: if control Ct = 28 and treated Ct = 25, the treated sample has roughly 2^3 = 8-fold more template.

## Slide 11
MODULE 01 · VARIANT
Real-Time PCR Chemistries — How the Signal Is Made
Two families of reporter. Non-specific dyes report the presence of any double-stranded DNA; sequence-specific probes report only the intended amplicon. The choice governs cost, specificity and whether multiplexing is possible.
A · Intercalating dye — SYBR Green I
Binds the minor groove of double-stranded DNA; fluorescence rises >1000-fold on binding. Free dye in solution is essentially dark.
Signal therefore increases with total dsDNA, whatever its sequence.
✓ Cheap, works with any validated primer pair, no probe design needed.
✕ Reports primer-dimers and non-specific products as if they were target — so a MELT (dissociation) CURVE after the run is mandatory: a single sharp Tm peak = one product.
✕ Cannot multiplex; signal also depends on amplicon length.
B · Hydrolysis probe — TaqMan
A third oligo binds between the primers, carrying a 5′ reporter (FAM, VIC, HEX) and a 3′ quencher (TAMRA, BHQ, or a non-fluorescent MGB quencher).
While the probe is intact, FRET quenches the reporter — no signal.
During extension, Taq’s 5′→3′ exonuclease hydrolyses the bound probe, physically separating reporter from quencher → fluorescence.
✓ Signal only from the true amplicon; different dyes allow 3–5 targets per tube (multiplex); no melt curve needed.
✕ Costly; probe must be designed and validated per target.
Chemistry | How signal arises | Specificity | Multiplex | Relative cost | Melt curve required
SYBR Green I | Intercalation into any dsDNA | Primer-dependent only | No | Low | Yes — essential
TaqMan (hydrolysis) | 5′ exonuclease cleavage of the probe | High — 3 oligos must match | Yes (3–5 dyes) | High | No
Molecular beacon | Stem-loop opens on hybridisation, unquenching | High — discriminates single-base mismatch | Yes | High | No
Scorpion primer | Probe tethered to the primer; unimolecular hybridisation | High, and kinetically very fast | Yes | High | No
FRET / hybridisation pair | Two adjacent probes bring donor and acceptor together | High; melt analysis for genotyping | Limited | High | Optional
Notes: The exonuclease requirement is why TaqMan will not work with a proofreading-only enzyme lacking 5′-3′ exo activity.

## Slide 12
MODULE 01 · VARIANT
Turning Ct Into a Number — Absolute and Relative Quantification
Two questions, two methods. "How many copies are in this tube?" needs a standard curve. "How much more is expressed in treated than in control?" needs only a reference gene and a calibrator sample.
Chart: Starting copy number (log scale)
| 10² | 10³ | 10⁴ | 10⁵ | 10⁶ | 10⁷
Ct | 32.6 | 29.3 | 26 | 22.7 | 19.4 | 16.1
Standard curve: slope −3.32, E = 100 %, R² = 0.999
Absolute quantification — the standard curve
Run a 10-fold dilution series of a standard of known copy number (plasmid, gBlock, or in vitro transcript) alongside the unknowns.
Plot Ct (y) against log₁₀ quantity (x): the relationship is linear across the dynamic range.
Efficiency: E = 10^(−1/slope) − 1. A slope of −3.32 corresponds to exactly 100 % efficiency (perfect doubling).
Acceptance criteria: efficiency 90–110 % (slope −3.6 to −3.1) and R² ≥ 0.98.
Report according to the MIQE guidelines (2009) — efficiency, dynamic range, replicates and reference-gene validation must all be stated.
Relative quantification — the Livak (2−ΔΔCt) method
ΔCt = Ct(target gene) − Ct(reference gene) — normalises for input amount
ΔΔCt = ΔCt(treated) − ΔCt(control / calibrator)
Fold change = 2^(−ΔΔCt)
Valid ONLY if target and reference amplify with near-identical efficiency (slopes differing by < 0.1). Where they do not, use the Pfaffl equation, which carries each gene’s own efficiency.
Getting normalisation right
Reference (“housekeeping”) genes — GAPDH, ACTB, 18S rRNA, TBP, RPL13A — must be validated as stable in YOUR treatment; GAPDH famously changes with hypoxia and glycolytic state.
Best practice: geometric mean of 2–3 validated reference genes (geNorm, NormFinder).
Always run technical triplicates, a no-template and a no-RT control, and inspect the melt curve when using SYBR Green.
Notes: Work one numerical example live: slope -3.32 gives 10^(1/3.32) = 2.00, i.e. doubling, i.e. 100% efficiency.

## Slide 13
MODULE 01 · CLARIFICATION
Untangling the Names — and Where Digital PCR Fits
The abbreviations RT-PCR, real-time PCR and qRT-PCR are constantly confused. They answer different questions and the confusion is purely one of naming, not of biology.
RT-PCR
REVERSE TRANSCRIPTION PCR. Template = RNA. An RT step makes cDNA, then ordinary PCR. Read out at the END POINT, usually on a gel. Answers: "is this transcript present?" NOT quantitative.
Real-time PCR = qPCR
QUANTITATIVE PCR. Template = DNA. Fluorescence measured EVERY CYCLE. Answers: "how much DNA was there to start with?" Quantitative, closed-tube, no gel.
RT-qPCR (qRT-PCR)
BOTH steps combined. Template = RNA → cDNA → real-time detection. Answers: "how much of this transcript is there?" The workhorse of gene-expression analysis. MIQE prefers the spelling RT-qPCR.
dPCR / ddPCR
DIGITAL PCR. Sample partitioned into ~20,000 droplets or wells, each with 0 or 1 template. End-point +/− scoring, then Poisson statistics give ABSOLUTE copies — no standard curve at all.
Attribute | Conventional / end-point PCR | Real-time qPCR | Digital PCR (dPCR / ddPCR)
Reaction volume | One bulk reaction | One bulk reaction | Partitioned into 20,000–10⁶ nanolitre compartments
When is signal read | Only after cycling, on a gel | Every cycle, during the exponential phase | Once, at end point — each partition scored positive or negative
Quantification | None (plateau erases differences) | Relative, or absolute against a standard curve | Absolute, from the fraction of negative partitions via Poisson statistics
Standard curve needed | n/a | Yes, for absolute quantification | No — its principal advantage
Tolerance to inhibitors / efficiency loss | Poor | Moderate — efficiency changes bias the result | High — end-point scoring is insensitive to modest efficiency loss
Best suited to | Presence/absence, cloning, genotyping, screening | Expression profiling, viral load, pathogen detection, SNP assays | Rare-allele and low-frequency mutation detection, copy-number variation, NGS library quantification, liquid biopsy
Notes: If students remember only one line: RT = reverse transcription (what the template is), q/real-time = quantitative (when you look).

## Slide 14
MODULE 01 · SUMMARY
Master Comparison — All PCR Formats Side by Side
Format | Template | Primers / detection | Quantitative? | Principal strength | Principal limitation
Conventional PCR | DNA | One primer pair; agarose gel at end point | No | Simple, cheap, universal; the reference format | Plateau destroys quantitative information; gel handling
Hot-start PCR | DNA | One pair; polymerase blocked until 95 °C | No | Removes mispriming and primer-dimer formed at set-up | Costlier enzyme; needs a long activation step
Nested PCR | DNA | Two pairs used sequentially (outer then inner) | No | Highest sensitivity and specificity; rescues low-copy, degraded targets | Severe carry-over contamination risk; two rounds of work
Multiplex PCR | DNA | Several primer pairs in one tube; sized on a gel or by dye | No | Several targets, one reaction — saves sample and time | Difficult to balance; primer cross-interaction; competition
RT-PCR | RNA | RT step, then one pair; end-point read-out | No (semi at best) | Detects transcripts and RNA-virus genomes | Needs intact RNA; no-RT control essential; not quantitative
Real-time PCR (qPCR) | DNA | SYBR Green or a labelled probe; read every cycle | Yes | Wide dynamic range, closed tube, high throughput, no gel | Instrument cost; efficiency must be validated; amplicon size limited
RT-qPCR | RNA | RT step + real-time detection | Yes | Standard method for gene-expression quantification | Combines the error sources of both steps; normalisation critical
Digital PCR | DNA or cDNA | Partitioned end-point scoring + Poisson statistics | Yes — absolute | No standard curve; superb precision for rare targets | Expensive; narrow dynamic range per run; lower throughput
Other notable variants | DNA | Inverse (unknown flanks) · Touchdown (falling Ta) · Colony · AS-PCR / ARMS (SNPs) · LAMP (isothermal) | — | Each solves one specific structural problem | Each also inherits the limits of the parent format
Notes: Use this slide as a revision anchor; the two columns that matter for exam answers are quantitative? and principal limitation.

## Slide 15
02
Electrophoresis
The migration of charged molecules through a supporting medium under an applied electric field — the universal read-out step of molecular biology.
1
Physical principles — mobility, field strength, Joule heating
2
Agarose gel electrophoresis of nucleic acids
3
SDS-PAGE and the discontinuous (Laemmli) buffer system
4
Isoelectric focusing and 2D gel electrophoresis
5
A master comparison of every electrophoretic format

## Slide 16
MODULE 02 · PRINCIPLES
The Physics of Electrophoresis
A charged molecule placed in an electric field is pushed toward the opposite electrode. Frictional drag from the medium opposes it. Within milliseconds the two forces balance and the molecule moves at a constant velocity — and it is that steady velocity, not the force, that separates a mixture.
The governing equations
Field strength: E = V / d (volts per cm between the electrodes)
Driving force: F = q · E (q = net charge on the molecule)
Frictional drag: F = f · v where f = 6πηr for a sphere (Stokes), η = viscosity, r = radius
At steady state q·E = f·v, therefore v = qE / f
ELECTROPHORETIC MOBILITY μ = v / E = q / f (cm² V⁻¹ s⁻¹) — a property of the molecule and the medium, independent of the voltage applied.
The one idea that unifies the whole module
μ = q / f. Every electrophoretic method is an engineered decision about which of these two terms is allowed to vary.
Hold q/mass constant and let the sieving medium set f → separation by SIZE (agarose, SDS-PAGE).
Hold f roughly constant and let q vary with pH → separation by CHARGE / pI (isoelectric focusing, native PAGE).
Do both, in sequence and at right angles → 2D gel electrophoresis.
The sample
Net charge (set by pH), size, and shape. Compact molecules of equal mass migrate faster than extended ones because f is smaller.
The electric field
Higher voltage → faster runs but more Joule heat (Q = I²Rt), which causes band distortion, "smiling", diffusion and even melting of the gel. Nucleic acid gels run at 5–10 V/cm; protein gels are often cooled.
The buffer
pH fixes the net charge of proteins; ionic strength is a trade-off — high I gives sharp bands but carries more current and more heat; low I gives less heat but broader zones and drifting pH.
The support medium
Pore size determines sieving. Agarose gives large pores for nucleic acids; polyacrylamide gives small, tunable pores for proteins. Electro-endosmosis (EEO) in charged media such as paper opposes migration.
Four variables that control every run
Notes: Joule heating is the practical limit on run speed; it explains smiling bands and why large-format gels are run overnight at low voltage.

## Slide 17
MODULE 02 · NUCLEIC ACIDS
Agarose Gel Electrophoresis — Workflow
DNA carries one negative charge per phosphate, so its charge-to-mass ratio is essentially constant regardless of length. Charge therefore cannot separate DNA — the gel does, by acting as a molecular sieve. Migration distance is proportional to −log₁₀(base pairs) over the resolving range.
1
Cast the gel
Boil agarose in TAE or TBE, cool to ~55 °C, add stain, pour into a tray with a comb; set 30–45 min.
2
Submerge & load
Place in the tank, cover with the SAME buffer, remove comb; mix samples with 6× loading dye and pipette into wells.
3
Run
5–10 V/cm. DNA migrates from the black cathode toward the red anode — "run to red". Stop before the dye front exits.
4
Visualise
UV (302 nm) or blue-light transilluminator; EtBr, SYBR Safe or GelRed fluoresce in proportion to bound DNA.
5
Interpret / recover
Size against a ladder, read negative and positive controls first, then excise and gel-purify if the band is needed.
The loading dye does three jobs
Glycerol or Ficoll — density, so the sample sinks into the well rather than diffusing away.
Bromophenol blue — tracking dye, co-migrates with roughly a 300 bp fragment in a 1 % gel.
Xylene cyanol — the slower dye, roughly 4 kb in a 1 % gel.
EDTA — chelates Mg²⁺ and stops any residual nuclease activity.
Conformation changes the answer
For the SAME plasmid, migration order is: supercoiled (covalently closed circular) — fastest, most compact; then LINEAR; then open-circular / nicked — slowest.
This is why an uncut plasmid prep shows several bands and why apparent "size" from an uncut plasmid is meaningless.
Single-stranded and highly structured RNA must be run denaturing (formaldehyde or glyoxal) before size is meaningful.
Applications
Checking PCR products — presence, size, specificity, primer-dimer.
Restriction digestion analysis and mapping; verifying clones.
Assessing genomic DNA integrity and RNA quality (28S:18S ratio).
Preparative recovery of a fragment for cloning or sequencing.
The separation step in Southern and northern blotting.
PFGE (alternating fields) extends the range to whole chromosomes, >50 kb up to ~10 Mb.
Notes: Emphasise "run to red" and the conformation order - both are standard viva questions.

## Slide 18
MODULE 02 · NUCLEIC ACIDS
Agarose Gels — Choosing the Conditions
Three choices decide the quality of a nucleic-acid gel: how much agarose, which buffer, and which stain. Each is a trade-off, not a default.
Agarose (% w/v) | Optimal resolving range | Typical use
0.3 % | 5 – 60 kb | Large genomic fragments; fragile, hard to handle
0.5 % | 1 – 30 kb | Large restriction fragments, lambda digests
0.7 % | 0.8 – 12 kb | Plasmid analysis, general cloning work
1.0 % (default) | 0.5 – 10 kb | Routine PCR products and digests
1.2 % | 0.4 – 7 kb | Smaller PCR products
1.5 % | 0.2 – 3 kb | Short amplicons, RFLP fragments
2.0 – 3.0 % | 0.05 – 2 kb | Very small fragments; use low-melt or NuSieve agarose
Higher percentage = smaller pores = better resolution of small fragments, but slower migration and harder recovery.
TAE versus TBE
TAE (Tris–acetate–EDTA): lower ionic strength and buffering capacity, so it exhausts on long runs — but DNA recovered from it is fully compatible with ligases, polymerases and transformation. Better for fragments > 12 kb, and the choice for preparative gels.
TBE (Tris–borate–EDTA): higher buffering capacity, sharper resolution of small fragments, better for long or high-voltage runs — but borate complexes cis-diols and inhibits many downstream enzymes, so it is an analytical-only buffer.
Stains and detection
Ethidium bromide — intercalates between base pairs; fluoresces ~20-fold more when bound; visualised at 302 nm. Sensitive (~5 ng) and cheap, but a potent mutagen requiring controlled disposal.
SYBR Safe / GelRed / GelGreen — blue-light-excitable, far less mutagenic, no UV damage to DNA destined for cloning.
SYBR Gold — highest sensitivity, works on ssDNA and RNA.
Methylene blue / crystal violet — no UV needed, safe for teaching labs, but 10–50× less sensitive.
Silver staining — for polyacrylamide gels of small fragments.
Common faults and their causes
Smiling / distorted bands → too much voltage, Joule heating, or uneven buffer depth.
Smeared lanes → overloaded DNA, degraded sample, or old buffer.
Bands running anomalously → wrong buffer strength, or supercoiled/nicked conformers.
No bands at all → dye front run off, gel run in water, or reversed electrodes.
Notes: The TAE/TBE distinction (recovery vs resolution) is worth a full minute; students routinely pick the wrong one for preparative work.

## Slide 19
MODULE 02 · PROTEINS
SDS-PAGE — Making Proteins Separate by Size Alone
Native proteins differ in charge, size AND shape, so their mobilities are uninterpretable. SDS-PAGE abolishes two of those three variables, leaving only size to determine migration.
DETERGENT
SDS binds ≈ 1.4 g per g protein
About one SDS molecule per two amino acid residues. Its intrinsic charge is swamped by the sulphate groups, giving every protein essentially the SAME charge-to-mass ratio.
REDUCTION
β-mercaptoethanol or DTT
Breaks inter- and intra-chain disulphide bonds so multimers dissociate into their constituent polypeptides.
DENATURATION
Heat 95 °C, 5 min
Unfolds tertiary and quaternary structure. Every protein becomes an extended SDS–polypeptide rod of similar shape — so the frictional coefficient now scales only with length.
SIEVING
Polyacrylamide mesh
The gel retards long rods more than short ones. Relative mobility Rf plotted against log₁₀(molecular weight) is linear — the basis of MW estimation.
The gel matrix
Acrylamide + N,N′-methylenebisacrylamide co-polymerise into a cross-linked mesh.
APS (ammonium persulphate) supplies free radicals; TEMED catalyses their formation. Oxygen inhibits — hence degassing and overlaying.
%T = total monomer, %C = proportion that is cross-linker. Both set pore size.
Unpolymerised acrylamide is a potent neurotoxin — always handle with gloves.
Gel (%T) | Linear range (kDa)
15 % | 10 – 43
12 % | 12 – 60
10 % | 20 – 80
7.5 % | 36 – 94
4–20 % gradient | 5 – 250
Anomalous migration: heavily glycosylated, very acidic/basic, and hydrophobic membrane proteins bind SDS abnormally and give incorrect apparent masses.
Detecting the bands
Coomassie Brilliant Blue R-250 — ~50 ng per band; simple, quantitative enough for most work.
Colloidal Coomassie G-250 — ~10 ng, MS-compatible.
Silver stain — ~1 ng, extremely sensitive but non-linear and can interfere with mass spectrometry.
SYPRO Ruby / Flamingo — fluorescent, ~1 ng, wide linear range, MS-friendly.
Zinc–imidazole negative staining — reversible, for preparative recovery.
Western blotting — transfer to PVDF/nitrocellulose, then antibody detection for identity and abundance.
Notes: Native PAGE keeps activity and quaternary structure and is the right choice for zymography and EMSA - contrast it here.

## Slide 20
MODULE 02 · PROTEINS
The Laemmli Discontinuous Buffer System — Why Bands Are Sharp
A sample loaded in 20 µL fills several millimetres of well, yet the bands are razor-thin. That is not the sieving gel’s doing — it is isotachophoresis in the stacking gel, driven by three deliberate discontinuities: in gel pore size, in pH, and in buffer ions.
Layer | Composition | pH | Role
Stacking gel | 4–5 %T acrylamide, Tris-HCl | 6.8 | Large pores — no sieving. Concentrates the sample into a thin starting zone
Resolving gel | 8–15 %T acrylamide, Tris-HCl | 8.8 | Small pores — sieves the stacked proteins by size
Tank (running) buffer | Tris–glycine + 0.1 % SDS | 8.3 | Supplies glycine, the trailing ion; SDS keeps proteins saturated
The stacking mechanism, step by step
Two ions of very different mobility
Chloride from the gel buffer is the LEADING ion — small and fully charged. Glycine from the tank is the TRAILING ion; at pH 6.8 it is largely a zwitterion with almost no net charge, so its mobility is very low.
A voltage gradient forms
Cl⁻ races ahead, leaving a zone depleted of charge carriers behind it. Resistance there rises, so the local voltage gradient becomes steep — the Kohlrausch discontinuity — which accelerates the slow glycinate to match the chloride front.
Proteins are stacked
SDS-coated proteins have mobilities between Cl⁻ and glycinate, so they are trapped between the two moving boundaries and compressed into a stack of micrometre-thin discs, ordered by mobility.
Unstacking at pH 8.8
Entering the resolving gel, glycine ionises fully; its mobility jumps and glycinate overtakes the proteins. The uniform field is restored, stacking ends, and every protein begins sieving from the same sharp start line.
Related buffer systems
Tris–tricine (Schägger–von Jagow) replaces glycine with tricine and resolves peptides below 20 kDa, where Laemmli gels fail. · Bis-Tris gels run near neutral pH, so the gel does not hydrolyse and shelf life is long; paired with MES buffer for small proteins and MOPS for large. · Continuous (single-buffer) systems are simpler but give broad bands, because there is no stacking step.
Notes: This is the hardest concept in the module. Anchor it on the two-ion sandwich: proteins are trapped between a fast leading ion and a slow trailing ion.

## Slide 21
MODULE 02 · PROTEOMICS
Two-Dimensional Gel Electrophoresis — Workflow
Two independent (orthogonal) properties, separated in sequence at right angles: isoelectric point along the horizontal axis, then molecular weight down the vertical axis. Because the two criteria are uncorrelated, resolving power multiplies rather than adds.
SAMPLE PREPARATION — lyse in 7 M urea + 2 M thiourea, 2–4 % CHAPS, DTT, carrier ampholytes and protease inhibitors. Remove salts, lipids and nucleic acids (they cause horizontal streaking).
FIRST DIMENSION — ISOELECTRIC FOCUSING. Load onto an IPG strip by passive or active rehydration; focus at up to 8,000 V to a total of 20–100 kVh. Each protein stops where the gel pH equals its pI.
EQUILIBRATION I (15 min) — 2 % SDS, 6 M urea, 30 % glycerol, 50 mM Tris-HCl pH 8.8 + 1 % DTT. Saturates proteins with SDS and reduces disulphide bonds.
EQUILIBRATION II (15 min) — the same buffer with 2.5 % iodoacetamide replacing DTT. Alkylates free cysteines so they cannot re-oxidise; prevents vertical point-streaking.
SECOND DIMENSION — SDS-PAGE. The strip is laid across the top of a slab gel and sealed with 0.5 % agarose; proteins migrate down and separate by molecular weight.
VISUALISATION — Coomassie, silver, SYPRO Ruby, or pre-electrophoretic Cy-dye labelling (2D-DIGE). Then image analysis: spot detection, gel-to-gel matching, normalisation, statistics.
IDENTIFICATION — excise the spot, in-gel trypsin digestion, and mass spectrometry (MALDI-TOF peptide mass fingerprint, or LC-MS/MS) against a sequence database.
Reading the finished gel
Horizontal axis = pI, acidic on the left, basic on the right (typically pH 3–10).
Vertical axis = molecular weight, large at the top, small at the bottom.
A horizontal "charge train" of spots at constant MW indicates post-translational modification — phosphorylation, deamidation, glycosylation.
Spot intensity is a semi-quantitative measure of abundance.
2D-DIGE — the modern refinement
Up to three samples are labelled before running with size- and charge-matched fluorophores: Cy2, Cy3 and Cy5.
All three are run on ONE gel, so gel-to-gel variation — the historic weakness of 2D-PAGE — is eliminated.
Cy2 typically carries a pooled internal standard present on every gel, allowing rigorous cross-gel normalisation.
Detection limit ~0.2 ng, with 4–5 logs of linear dynamic range.
Notes: The two equilibration steps are frequently examined: DTT reduces, iodoacetamide alkylates, and the order cannot be reversed.

## Slide 22
MODULE 02 · PROTEOMICS
Isoelectric Focusing in Detail — Strengths and Limits of 2D-PAGE
IEF is the only electrophoretic method that is a true equilibrium technique: molecules do not simply migrate, they converge on a fixed position and stay there. That is why its bands are so sharp and why it can resolve proteins differing by ~0.01 of a pH unit.
How focusing works
Proteins are ampholytes — their net charge depends on pH. Below its pI a protein is net positive, above its pI net negative.
In a stable pH gradient a protein migrates until it reaches the pH equal to its pI, where net charge is zero and migration stops.
Diffusion away from that point regains charge and drives the protein back — the zone is SELF-SHARPENING and stable at equilibrium.
Resolution improves with narrower gradients: "zoom" strips of pH 4.2–4.4 separate what a pH 3–10 strip cannot.
Carrier ampholytes versus immobilised pH gradients (IPG)
CARRIER AMPHOLYTES — small synthetic polyamino-polycarboxylic acids that form the gradient themselves under the field. Cheap, but the gradient DRIFTS toward the cathode during long runs, so reproducibility and basic-protein recovery are poor.
IPG STRIPS — Immobiline acrylamido buffers are covalently copolymerised into the gel, so the gradient is fixed. No drift, excellent gel-to-gel reproducibility, tailor-made and very narrow ranges possible, and much higher protein loading. IPG is the modern standard.
Strength of 2D-PAGE | Corresponding limitation
Resolves ~2,000–10,000 spots on a large-format gel — still the highest-resolution protein separation available | Labour-intensive, slow, and demanding of technical skill; a full experiment takes days
Separates protein ISOFORMS and post-translationally modified forms that MS of a digest alone would merge | Poor with hydrophobic membrane proteins — they precipitate at their pI despite urea and CHAPS
Directly visualises relative abundance across the whole proteome at once | Very acidic (pI < 3), very basic (pI > 10), very large (>200 kDa) and very small (<10 kDa) proteins are lost
Provides intact protein spots that can be excised for MS identification | Dynamic range problem: abundant proteins such as albumin mask low-copy regulatory proteins
Compatible with DIGE multiplexing for rigorous quantitative comparison | Gel-to-gel variability without DIGE; quantification is semi-quantitative at best
Applications: biomarker discovery in serum, CSF and tissue · differential proteomics of treated versus control cells · detection and mapping of post-translational modifications · purity and isoform analysis of recombinant biopharmaceuticals · microbial and plant proteome mapping.
Notes: The dynamic-range problem is why 2D-PAGE was displaced by shotgun LC-MS/MS for deep proteomes, yet retained for isoform work.

## Slide 23
MODULE 02 · SUMMARY
Master Comparison — Electrophoretic Techniques
Technique | Separates on the basis of | Matrix | Typical sample | Range / resolution | Principal use
Agarose gel electrophoresis | Size only (charge:mass is constant) | Agarose, 0.3–3 % | DNA, RNA | 50 bp – 60 kb | PCR checks, digests, blotting, preparative recovery
Pulsed-field gel electrophoresis | Size, using periodic re-orientation of the field | Agarose, low % | Very large DNA | 50 kb – 10 Mb | Chromosome separation, bacterial strain typing
Native (non-denaturing) PAGE | Charge, size AND shape together; activity retained | Polyacrylamide | Folded proteins, complexes | Complex-dependent | Zymography, EMSA / gel shift, oligomeric state, native activity
SDS-PAGE | Molecular weight only | Polyacrylamide, 7.5–15 % | Denatured, reduced proteins | ~5 – 250 kDa | MW estimation, purity, the first step of western blotting
Isoelectric focusing (IEF) | Isoelectric point (pI) | IPG strip or ampholyte gel | Native or urea-solubilised proteins | Δ pI ≈ 0.01 unit | Charge isoforms, first dimension of 2D, protein characterisation
2D gel electrophoresis | pI first, then molecular weight (orthogonal) | IPG strip + polyacrylamide slab | Whole proteomes | 2,000–10,000 spots | Differential proteomics, PTM mapping, biomarker discovery
Capillary electrophoresis | Charge-to-size ratio in free solution or a polymer sieve | Fused-silica capillary | DNA fragments, proteins, small molecules | Single-base resolution | Sanger sequencing, fragment analysis, STR profiling, quality control
Notes: Column two is the one to memorise; every exam question on this module reduces to what property is being sorted.

## Slide 24
03
Centrifugation
Separation in an artificial gravitational field. A rotor converts rotational speed into a force thousands to a million times gravity, and particles sort by how fast — or how far — they sediment.
1
Principles — RCF, the Svedberg equation and rotor design
2
Differential centrifugation and subcellular fractionation
3
Rate-zonal density gradient centrifugation (separation by s value)
4
Isopycnic density gradient centrifugation (separation by buoyant density)
5
Gradient media, applications and a direct comparison

## Slide 25
MODULE 03 · PRINCIPLES
Sedimentation, RCF and the Svedberg Equation
A particle in a spinning rotor experiences an outward centrifugal field ω²r. Whether it moves outward, stays put, or floats depends on its mass, its density relative to the medium, and its shape.
The equations you must be able to use
Relative centrifugal field: RCF (× g) = 1.118 × 10⁻⁵ × r(cm) × (rpm)². Always quote g, never rpm alone — the same rpm in a wider rotor gives a much larger force.
Sedimentation velocity: v = ω²r · s
Svedberg equation: s = v /(ω²r) = m(1 − v̄ρ) / f, where m = particle mass, v̄ = partial specific volume, ρ = medium density, f = frictional coefficient.
One svedberg unit, 1 S = 10⁻¹³ seconds.
If ρ_medium > 1/v̄ the term (1 − v̄ρ) becomes negative and the particle FLOATS instead of sedimenting — the basis of flotation methods.
Why S values are not additive
The classic example: a 50S subunit plus a 30S subunit gives a 70S ribosome, not an 80S one.
s depends on mass AND on the frictional coefficient f, which is a function of size and shape.
When the two subunits associate, the complex becomes more compact than the sum of its parts: the mass adds, but f rises less than proportionally, so s increases sub-additively.
Same logic: eukaryotic 60S + 40S = 80S.
Consequence: an S value describes sedimentation behaviour, NOT molecular weight — two molecules of equal mass but different shape have different S values.
Rotor / class | Design | Path length | Best suited to
Fixed-angle rotor | Tubes held at 20–45° to the axis | Short | Rapid pelleting; differential centrifugation; self-forming CsCl gradients
Swinging-bucket rotor | Buckets swing to horizontal during the spin | Long | Rate-zonal gradients; sharp band resolution; sample layered on top
Vertical rotor | Tubes parallel to the axis of rotation | Shortest | Fastest isopycnic banding — the gradient forms across the tube diameter
Continuous-flow rotor | Sample fed in and out while spinning | — | Industrial-scale harvesting of cells and virus particles
Low-speed / benchtop | < 6,000 rpm, ≈ 6,000 × g | — | Whole cells, nuclei, crude precipitates
High-speed centrifuge | up to ~25,000 rpm, ≈ 60,000 × g, refrigerated | — | Mitochondria, chloroplasts, lysosomes, large membranes
Preparative ultracentrifuge | up to ~100,000 rpm, ≈ 800,000–1,000,000 × g; refrigerated and evacuated | — | Ribosomes, microsomes, viruses, nucleic acids, macromolecules
Analytical ultracentrifuge | Optical (UV / Schlieren / interference) detection during the spin | — | Sedimentation velocity and equilibrium runs → MW, purity, shape, association constants
Notes: Give the numerical habit: convert rpm to g before writing any method, and state the rotor.

## Slide 26
MODULE 03 · PREPARATIVE
Differential Centrifugation — Fractionating the Cell
The simplest preparative strategy: spin a homogenate at a low force, keep the supernatant, spin it harder, and repeat. Each step pellets everything that sediments faster than the chosen cut-off, so separation is essentially by SIZE (through the s value) in a uniform medium.
HOMOGENATE — tissue disrupted in ice-cold isotonic 0.25 M sucrose, 10 mM Tris pH 7.4, 1 mM EDTA + protease inhibitors. Cold and isotonic to keep organelles intact.
600 – 1,000 × g, 10 min → PELLET: nuclei, unbroken cells, cytoskeletal debris. (Supernatant carried forward.)
10,000 – 15,000 × g, 20 min → PELLET: mitochondria, lysosomes, peroxisomes, chloroplasts — the "heavy organelle" fraction.
100,000 × g, 60 min → PELLET: microsomes — vesicles of endoplasmic reticulum and plasma membrane, Golgi, and large polysomes.
100,000 × g, 2 h → PELLET: ribosomes and ribosomal subunits, small polysomes, large soluble complexes.
FINAL SUPERNATANT = cytosol: soluble enzymes, tRNA, metabolites.
The built-in limitation
Every pellet contains not only its target but everything larger that has not yet been removed, plus material physically trapped as the pellet forms.
Fractions are therefore CRUDE and cross-contaminated. Re-suspending and re-pelleting (washing) improves purity at the cost of yield.
Resolution is low because the whole tube has one uniform density — nothing prevents fast particles from sweeping slow ones down with them.
For clean fractions, follow with a density-gradient step.
Marker enzymes — how purity is proved
Nuclei — DNA content, lamin B
Mitochondria — succinate dehydrogenase, cytochrome c oxidase
Lysosomes — acid phosphatase, β-hexosaminidase
Peroxisomes — catalase, urate oxidase
Endoplasmic reticulum — glucose-6-phosphatase, NADPH-cytochrome c reductase
Golgi — galactosyltransferase
Plasma membrane — Na⁺/K⁺-ATPase, 5′-nucleotidase
Cytosol — lactate dehydrogenase
Notes: Marker enzymes are the classical answer to "how do you know your fraction is pure?" - expect this in a viva.

## Slide 27
MODULE 03 · PREPARATIVE
Density Gradient Centrifugation — Rate-Zonal versus Isopycnic
A density gradient in the tube stabilises the separated zones against convection and mixing. Two quite different experiments use that same gradient: one stopped early to sort by SPEED, one run to completion to sort by DENSITY.
Rate-zonal (velocity) centrifugation
A thin band of sample is layered ON TOP of a shallow preformed gradient (e.g. 5–20 % sucrose).
The particle is DENSER than the medium everywhere in the tube, so it never stops on its own.
Separation is by sedimentation coefficient — a function of size, mass and shape.
NON-EQUILIBRIUM: the run must be stopped before the fastest band reaches the bottom. Timing is critical.
Swinging-bucket rotor, long path length.
Isopycnic (equilibrium, buoyant-density) centrifugation
A steep gradient spans the densities of the particles; sample may be layered on top, underneath, or mixed uniformly throughout (self-forming CsCl).
Each particle migrates until the medium density equals its own — where (1 − v̄ρ) = 0 — and then stops.
Separation is by BUOYANT DENSITY ALONE; size affects only how fast equilibrium is reached, not where the band ends up.
EQUILIBRIUM: once banded, longer spinning does not change the result.
Point of comparison | Differential | Rate-zonal | Isopycnic
Basis of separation | Sedimentation rate in a uniform medium (mainly size) | Sedimentation coefficient s (size, mass, shape) | Buoyant density of the particle
Medium | Uniform buffer, no gradient | Shallow gradient, less dense than every particle | Steep gradient spanning the particle densities
Sample application | Mixed throughout the tube | Thin layer on top of the gradient | On top, at the bottom, or mixed throughout
Equilibrium reached? | No — pelleting continues | No — must stop the run at the right moment | Yes — self-limiting and time-independent once banded
Product | Pellet + supernatant | Discrete zones suspended in the gradient | Sharp bands at their isopycnic positions
Typical media | — | Sucrose 5–20 %, glycerol, iodixanol | CsCl 1.55–1.80 g/cm³, Percoll, iodixanol, sucrose, KBr
Resolution | Low — cross-contaminated pellets | High for particles of similar density but different size | Highest resolution by density; insensitive to particle size
Classic applications | Subcellular fractionation of tissue homogenates | Polysome profiling, separating 30S/50S/70S ribosomes, rRNA and mRNA, protein complexes | Supercoiled plasmid vs genomic DNA in CsCl–EtBr; ¹⁵N/¹⁴N DNA in the Meselson–Stahl experiment; full vs empty AAV capsids; lymphocytes on Ficoll-Paque
Notes: Meselson-Stahl is the single best illustration of isopycnic separation; polysome profiling is the best for rate-zonal.

## Slide 28
04
Radioisotope
Tracer Techniques
A radiolabelled molecule is chemically identical to its unlabelled counterpart, so it follows exactly the same biological path — but can be detected at concentrations far too low to perturb the system.
1
The tracer principle, decay, units and specific activity
2
The isotopes actually used in biology and what each is used for
3
Detection — Geiger–Müller, scintillation counting, autoradiography, phosphorimaging
4
Landmark experiments and routine applications
5
Radiation safety and non-radioactive alternatives

## Slide 29
MODULE 04 · PRINCIPLES
The Tracer Principle, Decay and Units
Isotopes of an element share its chemistry but differ in neutron number. Substituting a radioactive isotope into a biomolecule therefore changes nothing biologically, yet makes that molecule individually traceable through any pathway, at picomolar concentrations that leave pool sizes undisturbed.
Decay and its mathematics
Modes: α (heavy, non-penetrating), β⁻ (electron), β⁺ (positron), γ (photon), and electron capture.
Decay is first-order and random: N = N₀ e^(−λt)
Half-life: t½ = 0.693 / λ — a constant, unaffected by temperature, pressure or chemical state.
Units of activity
Becquerel (Bq) — SI unit; 1 Bq = 1 disintegration per second.
Curie (Ci) — 1 Ci = 3.7 × 10¹⁰ Bq (the activity of 1 g of ²²⁶Ra).
Counts per minute (cpm) is what an instrument records; disintegrations per minute (dpm) is the true activity — cpm/dpm = counting efficiency.
Absorbed dose: gray (Gy); dose equivalent: sievert (Sv).
Specific activity — the key practical number
Activity per unit amount of substance, e.g. Ci/mmol or Bq/mol.
It sets the detection limit: a high-specific-activity probe gives signal from fewer molecules.
Trade-off — high specific activity also means faster radiolysis of the labelled compound and a shorter usable life.
Isotope dilution: adding known labelled material lets an unknown pool size be calculated.
Isotope | Half-life | Emission (max energy) | Typical labelled compound | What it is used for | Detection of choice
³H (tritium) | 12.3 years | β⁻, very weak, 18.6 keV | [³H]thymidine, [³H]leucine, [³H]uridine, [³H]ligands | DNA synthesis and cell proliferation; protein turnover; receptor binding | Liquid scintillation counting; fluorography for gels (film alone is too insensitive)
¹⁴C | 5,730 years | β⁻, weak, 156 keV | ¹⁴CO₂, [¹⁴C]glucose, [¹⁴C]amino acids | Metabolic and biosynthetic pathway tracing; carbon dating | Liquid scintillation counting; fluorography; phosphorimaging
³²P | 14.3 days | β⁻, high energy, 1710 keV | [γ-³²P]ATP, [α-³²P]dCTP | 5′ end-labelling of probes, nick translation, random priming, kinase assays, EMSA | Autoradiography with intensifying screens at −70 °C; phosphorimaging; Cerenkov counting
³³P | 25.4 days | β⁻, medium, 249 keV | [α-³³P]dATP | DNA sequencing and in situ work needing sharper images than ³²P | Autoradiography — better resolution and safer than ³²P
³⁵S | 87.4 days | β⁻, weak, 167 keV | [³⁵S]methionine, [³⁵S]cysteine, [α-³⁵S]dATP | Pulse-chase labelling of newly synthesised protein; Sanger sequencing | Autoradiography / fluorography; liquid scintillation counting
¹²⁵I | 59.4 days | γ and X-rays via electron capture, 35 keV | Iodinated hormones, antibodies and peptides (chloramine-T, Bolton–Hunter) | Radioimmunoassay (RIA), receptor-binding studies, protein iodination | Solid scintillation "gamma counter" — NaI(Tl) crystal
Notes: The pairing to remember: 32P labels nucleic acid (phosphate backbone), 35S labels protein (methionine/cysteine) - exactly the Hershey-Chase logic.

## Slide 30
MODULE 04 · PRACTICE
Detection Methods, Applications and Safety
Choosing a detector is a matter of matching it to the emission energy: weak β emitters such as ³H must be counted in intimate contact with a scintillator, whereas high-energy ³²P can be imaged through a film or a storage plate.
A
Geiger–Müller counter
Gas ionisation in a tube; an audible/rate read-out. Used for survey monitoring of benches, hands and waste. Good for ³²P, essentially blind to ³H.
B
Liquid scintillation counting
Sample dissolved in a cocktail of solvent + fluor (PPO/POPOP). β energy → solvent → fluor → photons → photomultiplier → cpm. The only practical route for ³H and ¹⁴C. Chemical and colour QUENCHING must be corrected (channels-ratio or external standard) to convert cpm to dpm.
C
Solid scintillation (gamma counter)
A NaI(Tl) crystal converts γ photons to light. No sample preparation, non-destructive. The standard for ¹²⁵I in RIA.
D
Autoradiography & fluorography
The gel or blot is placed against X-ray film. Intensifying screens at −70 °C amplify ³²P signal; fluorography (impregnating the gel with PPO) is required for weak emitters (³H, ¹⁴C, ³⁵S). Film response is non-linear and saturates.
E
Phosphorimaging
A BaFBr:Eu²⁺ storage plate traps the energy; a laser then releases it as light. Linear over ~5 orders of magnitude, 10–100× faster than film, and directly quantitative — the modern replacement for autoradiography.
Landmark and routine applications
Hershey & Chase (1952) — ³²P labelled phage DNA, ³⁵S labelled phage coat protein; only ³²P entered the bacterium, proving DNA is the genetic material.
Calvin & Benson — ¹⁴CO₂ pulses into algae revealed the path of carbon in photosynthesis.
Palade’s pulse–chase with [³H]leucine mapped the secretory pathway ER → Golgi → vesicle.
[³H]thymidine incorporation to measure S-phase entry and cell proliferation.
Radioimmunoassay (Yalow & Berson) — ¹²⁵I tracer competition, sensitive enough for peptide hormones.
End-labelled ³²P probes for Southern, northern and western blots, EMSA, DNase-I footprinting and Maxam–Gilbert sequencing.
In vivo imaging: ¹⁸F-FDG PET, ⁹⁹ᵐTc scintigraphy, ¹³¹I thyroid therapy.
Radiation safety — ALARA
TIME — minimise exposure duration.
DISTANCE — inverse-square law; use tongs, never fingers.
SHIELDING — 1 cm Perspex/acrylic for ³²P β (lead would generate bremsstrahlung); lead for γ.
Designated area, drip trays, no mouth pipetting, dedicated glassware.
Film or TLD badges and ring dosimeters; regular Geiger surveys and wipe tests.
Waste: decay-in-storage for short half-lives; licensed disposal otherwise.
Non-radioactive alternatives
Digoxigenin (DIG)–labelled probes with anti-DIG–alkaline phosphatase.
Biotin–streptavidin systems.
Fluorescent dyes (Cy3/Cy5, Alexa) — the basis of qPCR, DIGE and microarrays.
Chemiluminescence (HRP + luminol) for western blots.
Advantages: no licence, no half-life, no waste problem, multiplexing. Radioisotopes still win on absolute sensitivity and true linearity.
Notes: Note the Perspex-not-lead point for 32P: lead shielding generates bremsstrahlung X-rays and makes matters worse.

## Slide 31
WRAP-UP
What to Carry Away
Four families, one question each. If you can answer the question in the second column for any technique put in front of you, you understand it.
Family | The question it answers | The property it exploits | The single most confused point
PCR and its variants | Is this sequence present, and how much of it was there to begin with? | Sequence complementarity of two primers, plus exponential doubling | RT- means reverse transcription (the template is RNA); q / real-time means quantitative (when you look). RT-qPCR is both
Nested PCR | Can I detect a target that ordinary PCR misses? | Two independent rounds of primer selection multiply specificity | Its sensitivity is also its danger — carry-over contamination gives false positives
Agarose gel electrophoresis | How big is this nucleic acid fragment, and is it pure? | Sieving, because charge-to-mass ratio is constant for DNA | Supercoiled DNA runs faster than linear DNA of the same size — conformation, not length
SDS-PAGE | What is the molecular weight and purity of this protein? | SDS imposes a uniform charge-to-mass ratio, so only size matters | Sharp bands come from the discontinuous stacking system, not from the resolving gel
2D gel electrophoresis | How does a whole proteome differ between two conditions? | pI and molecular weight are orthogonal, so resolving power multiplies | IEF is an equilibrium method; the second dimension is not
Differential centrifugation | Can I get a crude organelle fraction quickly? | Sedimentation rate in a uniform medium — effectively size | Pellets are always cross-contaminated; purity must be proved with marker enzymes
Density gradient centrifugation | Can I purify particles that differ subtly? | Rate-zonal sorts by s value; isopycnic sorts by buoyant density | Rate-zonal must be stopped in time; isopycnic reaches equilibrium and cannot over-run
Radioisotope tracers | Where does this molecule go, and how fast? | Chemical identity with the unlabelled molecule plus extreme detection sensitivity | ³²P labels nucleic acid (phosphate); ³⁵S labels protein (Met/Cys) — the basis of Hershey–Chase
Notes: Close by returning to the roadmap slide: amplify or separate, and always name the property being sorted.